ACTIA Automotive	XT018-F
MEMO	Page /

Robustness test :

I) canCheck
All the tests will be done on the card (PCM) .
The objective of canCheck is to check if all can frames are well received and if all data are correct : no missing element . This program will read the data in a text file .
a) can frames
Here is a procedure to follow :

Open terminal and connect to the card :

- Bring can0 interface up @500kbps
  ip link set up can0 type can bitrate 500000
- In a window, launch command :
  canCheck -f file.txt	→ add -S if file with timestamps is present
→ add -D for debug
→ file.txt is file containing the data to be	compared

canCheck integrated a function which compare data from one frame to another.
This is made possible by a counter which increments and then its' easier to check bytes by bytes.

canCheck should return an error if :
- data are not incremented correctly (return -1)
- data are in random mode (return -2)

Or return 0 , if all is correct !

canCheck -f candump_225_ok.txt

Expected result	Test
Return 0	OK

In debug Mode :
canCheck -f candump_225_ok.txt -D

Expected result	Test
Frame : can0 652 [8] 00 00 00 00 00 00 00 00 / Frame : can0 652 [8] 01 00 00 00 00 00 00 00 / Frame : can0 652 [8] 02 00 00 00 00 00 00 00 / Frame : can0 652 [8] 03 00 00 00 00 00 00 00 / Return 0	OK

a) Isotp frames
ISOTP frame is a protocol allows be useful for the transport of messages that exceed the eight bytes maximum payload of CAN frames.

Here is a procedure to follow :

Open terminal and connect to the card :

Bring can1 and can2 interface up @500kbps
ip link set up can0 type can bitrate 500000
ip link set up can1 type can bitrate 500000

Start isotp server (in one window)
isotprecv -s 701 -d 700 can1 -z 9 -l
→ isotprecv allows to receive only data
→ we can't see interface name, Id, data length
→ But we can use candump or wireshark to see the entire frame

Start a sniffer in an other window (still on the card) :
candump can1 can0 -z 7 > file.txt &

Start isotpgen
isotpgen -s 700 -d 701 can0 -z 9 -D i -T i -n 255

We have different options for this function : See below
- -D : send PDU with len bytes
    - : enter a number 1<nbr<4095
    - 'i' : incremented length
    - 'r' : random length

- -T : Data (payload) generation mode
    - 'i' : incremented data
    - 'r' : random data

We can juggle between the different options
isotpgen -s 700 -d 701 can0 -z 9 -D r -T I
isotpgen -s 700 -d 701 can0 -z 9 -D 4095

Expected result with isotpgen -s 700 -d 701 can0 -z 9 -D i -T I -n 255	Test
00 / 01 00 / 02 00 00 / 03 00 00 00 / 04 00 00 00 00 / 05 00 00 00 00 00 / 06 00 00 00 00 00 00 / 07 00 00 00 00 00 00 00 / […] [..]	OK

Now, open the file.txt :

	Test
can1 700 [2] 01 00 / can1 700 [3] 02 01 00 / can1 700 [4] 03 02 00 00 / can1 700 [5] 04 03 00 00 00 / can1 700 [6] 05 04 00 00 00 00 / can1 700 [7] 06 05 00 00 00 00 00 / can1 700 [8] 07 06 00 00 00 00 00 00 / can1 700 [8] 10 08 07 00 00 00 00 00 / can0 701 [3] 30 00 00 / can1 700 [3] 21 00 00 / [..] [..]	OK

Explanation :

As soon as, the message is longer than 7 bytes, we could see the first frame with the data length.
Then we have, the flow control frame from the receiver (701). And the consecutive frame (with a loop from 21 to 2F )

Then we can launch canCheck with the this file and check if all is well received

canCheck -f isotp.txt -i

N'ayant pas fini le soft pour comparer ces trames, je n'ai pas pu l'illustrer d'exemple de tests.