ACTIA Automotive	XT018-F
MEMO	Page /

Robustness test :

I) canCheck
All the tests will be done on the card (PCM) .
The objective of canCheck is to check if all can frames are well received and if all data are correct : no missing element . This program will read the data in a text file .
a) can frames
Order of commands :
- Bring can0 interface (card1 & card 2)
- Launch candump (card 2)
- Launch cangen (card 1)
Here is a procedure to follow : Open terminal and connect to the card

CARD 2

     Bring can0 interface up @500kbps
 ip link set up can0 type can bitrate 500000

     Launch CANGEN
 Candump can0 > file.txt **

CARD 1

     Bring can0 interface up @500kbps
 ip link set up can0 type can bitrate 500000

     Launch CANSEND
 cangen can0 -I 652 -L 8 -D i -z 7 **

Bus CAN

** We have different options for cangen → tape cangen -h to see everything
** file.txt corresponds to the file containing the frames send by cangen. We can choose the way where we want to register this file.

Then, when the file is filled, we can use canCheck on the card where is the frame file. Here, it's the card 2.
CanCheck works only with increment data.

In a window (here card 2), launch command :
canCheck -f file.txt	→ add -S if file with timestamps is present
→ add -D for debug
→ file.txt is file containing the data to be	compared

CanCheck integrated a function which compare data from one frame to another.
This is made possible by a counter which increments and then its' easier to check bytes by bytes.

CanCheck should return an error if :
- data are not incremented correctly (return CAN_CHECK_KO)
- data are in random mode (CAN_CHECK_ERROR_RANDOM)

Or return CAN_CHECK_OK , if all is correct !

canCheck -f candump_225_ok.txt

Expected result	Test
CAN_CHECK_OK	OK

In debug Mode :
canCheck -f candump_225_ok.txt -D

Expected result	Test
Frame : can0 652 [8] 00 00 00 00 00 00 00 00 / Frame : can0 652 [8] 01 00 00 00 00 00 00 00 / Frame : can0 652 [8] 02 00 00 00 00 00 00 00 / Frame : can0 652 [8] 03 00 00 00 00 00 00 00 / CAN_CHECK_OK	OK

b) Isotp frames
ISOTP frame is a protocol allows be useful for the transport of messages that exceed the eight bytes maximum payload of CAN frames.

Here is a procedure to follow : Open terminal and connect to the card

CARD 1
Bring can1 and can2 interface up @500kbps
 ip link set up can0 type can bitrate 500000
 ip link set up can1 type can bitrate 500000

     Start isotp server
 isotprecv -s 701 -d 700 can1 -z 9 -l

CARD 2
Bring can1 and can2 interface up @500kbps
 ip link set up can0 type can bitrate 500000
 ip link set up can1 type can bitrate 500000

     Star a sniffer
 candump can1 can0 -z 7 > file.txt &
     Then
 isotpgen -s 700 -d 701 can0 -z 9 -D i -T i -n 255

→ isotprecv allows to receive only data
→ we can't see interface name, Id, data length
→ But we can use candump or wireshark to see the entire frame
We have different options for this function : See below
- -D : send PDU with len bytes
    - : enter a number 1<nbr<4095
    - 'i' : incremented length
    - 'r' : random length

- -T : Data (payload) generation mode
    - 'i' : incremented data
    - 'r' : random data

We can juggle between the different options
isotpgen -s 700 -d 701 can0 -z 9 -D r -T I
isotpgen -s 700 -d 701 can0 -z 9 -D 4095

Expected result with isotpgen -s 700 -d 701 can0 -z 9 -D i -T I -n 255	Test
00 / 01 00 / 02 00 00 / 03 00 00 00 / 04 00 00 00 00 / 05 00 00 00 00 00 / 06 00 00 00 00 00 00 / 07 00 00 00 00 00 00 00 / […] [..]	OK

Now, open the file.txt :

	Test
can1 700 [2] 01 00 / can1 700 [3] 02 01 00 / can1 700 [4] 03 02 00 00 / can1 700 [5] 04 03 00 00 00 / can1 700 [6] 05 04 00 00 00 00 / can1 700 [7] 06 05 00 00 00 00 00 / can1 700 [8] 07 06 00 00 00 00 00 00 / can1 700 [8] 10 08 07 00 00 00 00 00 / can0 701 [3] 30 00 00 / can1 700 [3] 21 00 00 / [..] [..]	OK

Explanation :

As soon as, the message is longer than 7 bytes, we could see the first frame with the data length.
Then we have, the flow control frame from the receiver (701). And the consecutive frame (with a loop from 21 to 2F )

Then we can launch canCheck with the this file and check if all is well received

canCheck -f isotp.txt -i

N'ayant pas fini le soft pour comparer ces trames, je n'ai pas pu l'illustrer d'exemple de tests.